## Slide 1: Predicting streamflow and hydropower production with Long Short Term Memory models
25.04.2025
Ole Wulff (NORCE), Thea Roksvåg (Norsk Regnesentral), Kamilla Wergeland (Småkraft/UiB) & Silius Vandeskog (Norsk Regnesentral)

## Slide 2
1) NVE Q4 2024
Chart: 
| Upgrades | Solar | Wind power | Large scale hydro | Other new small scale hyro | Småkraft AS
Sales | 0.19 | 0.01 | 0 | 0.18 | 0.29 | 0.32
32 % of 1.039 GWh under construction
Upgrades
Solar
Wind power
Large scale hydro
Other, new small-scale hydro
Småkraft AS
Småkraft AS

## Slide 3: Småkraft AS in Climate Futures
Accurate estimations of past streamflow:
Power plant valuation for acquisitions
Expected production volumes for budgeting purposes
Portfolio uncertainty estimation (P10, P90)
Accurate forecast the next days to weeks:
Reduce imbalance costs
Plan maintenance with minimal downtime in production
Optimize production by exploiting regulation opportunities
Knowledge about future streamflow:
Identify the right project
Optimize future and existing power plants
Identify risks related to more extreme events
Future streamflow based on climate change
Short to mid-term forecast based on weather models
Historical streamflow based on observations and reanalysis

## Slide 4: Calculating production from streamflow
Streamflow (m3/s) to power production:
Power (kW) from streamflow:
Head loss (m) due to friction in the water way:
Velocity (m2/s):

## Slide 5: Back-calculated inflow from hydropower plants

## Slide 6: Recap: Our aim
Develop hydrological models that can predict streamflow (and thus also power production) in gauged and ungauged catchments
We develop two competing model types (one traditional, one data-driven)
Data:
  136 Småkraft catchments
    Only production data (censored for large streamflows)
    Short time series
  190 NVE catchments
    Streamflow data
    Long time series

## Slide 7: First model: HBV
Conceptual hydrological model
Most used model for simulating Norwegian streamflows by NVE
R implementation in the HBV.IANIGLA package
Input:
  Daily precipitation and temperature
  Elevation (hypsometric curves)
Made by Kolbjørn Engeland, NVE

## Slide 8: Calibration
Calibration must be performed separately, for each catchment
Different calibration methods for gauged and ungauged catchments
Gauged:
  Simulate streamflow (and maybe compute power production) from the HBV model
  Find parameters that maximise Nash-Sutcliffe efficiency (NSE) between simulated and observed data
  Optimisation method and initial parameter values chosen based on discussion with NVE
Ungauged:
  Regionalisation method based on donor catchments

## Slide 9: Donor-based regionalisation
Coordinates, size, climate conditions, gradient, river length, %forest, %mountain, %lakes
?
Ungauged
catchment
Gauged catchments with
calibrated HBV models

## Slide 10: Donor-based regionalisation
Coordinates, size, climate conditions, gradient, river length, %forest, %mountain, %lakes
?
Ungauged
catchment
Gauged catchments with
calibrated HBV models

## Slide 11: Donor-based regionalisation
Weather data
m^3/s
Date
Use the daily median of the five simulations as our final simulation

## Slide 12: Cross-validation
Gauged catchment performance:
  Training data from 1990-2020
  Test data from 2021-2023
Ungauged catchment performance:
  Use data from all but one catchments, to simulate streamflow in that catchment
Compare performance against seNorge avrenning, NVEs national gridded runoff data product (made from a regional HBV model)

## Slide 13: HBV results
NVE only
SeNorge avrenning
NVE + Småkraft
Småkraft only

## Slide 14: HBV results
NVE only
SeNorge avrenning
NVE + Småkraft
Småkraft only

## Slide 15: Switching to data-driven hydrological models
We have data from >300 catchments, but the conceptual model makes it impossible to use more than a fraction of these to predict streamflow
Data-driven models are made to use as much data as possible

## Slide 16: Second model: Long Short-Term Memory (LSTM)
Type of recurrent neural network
Has performed very well in the literature
Python implementation in the neuralhydrology package
Input:
  Daily precipitation and temperature
  Elevation (hypsometric curves)
  Static catchment covariates used for donor-matching with the HBV model
By fdeloche - Treball propi, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=60149410

## Slide 17: Calibration (model training)
Global calibration, using all available catchments (minus validation/test data)
Loss function:
  NVE data: Simulate streamflow and compute NSE
  Småkraft data: Simulate streamflow, compute power production, then compute NSE

## Slide 18: Results
NVE only
SeNorge avrenning
NVE + Småkraft
Småkraft only

## Slide 19: Results
NVE only
SeNorge avrenning
NVE + Småkraft
Småkraft only

## Slide 20: Discussion
LSTM beats HBV in most settings, even in gauged catchments
However:
  LSTM is a black box
  LSTM is not physically consistent
  Balancing NVE/Småkraft data in the LSTM is difficult, especially in the upper tail
Combining NVE/Småkraft data works, but not as well as we had hoped

## Slide 21: Future work – hourly streamflow forecast
Motivation:
Day-ahead nominations and imbalance costs
Production planning for power plants with small reservoirs
Data:
Hourly streamflow observations from NVE
Production data and back-calculated inflow from Småkraft
NORA3 atmosphere hindcast
MEPS ensemble forecast